## Slide 1: Optimization of Phased Array for RET-CR
Leo Deer
* This project overview is adopted from two presentation given to the RET collaboration. I’ve adapted it to be more accessible.

## Slide 2: Project overview
Build a piece of software that optimizes the design of a transmission phased array antenna (TX) for the Radar Echo Telescope experiment. That is, find the best parameters for the design of the phased array.
To do this, I simulated the electric field of a variety of phased array designs using numeric EM solvers and took that data to see which design will give the rest of the experiment the best results.

## Slide 3: RET overview
Radar Echo Telescope (RET) is a collaboration with the purpose of detecting ultra-high energy neutrinos in Antarctica.
When neutrinos come down from the atmosphere and hit the ice, they cause a dense in-ice cascade of particles. Radio waves have characteristic wavelengths such that they can reflect off these in-ice cascades.
So, RET designed an experiment to detect these reflections

## Slide 4: RET overview
A simplified version of the experiment goes like,
Use surface detectors to detect when and where there is an in-ice cascade.
Use a phased array transmission antenna (TX) to send out a signal directed at the surface.
That signal will bounce off the in-ice cascade and get detected by a receiver antenna (RX).

## Slide 5: More details on the transmission phased array
Azimuthal symmetry
8 dipoles (modeled as point like)
Inter-dipole separation of one (wavelength)
is the depth of the top dipole
is the angle at which the phased array is steered in vacuum from a phase factor applied to each antenna. The factor for the th dipole is:
  is the wavenumber of the antenna
  is the inter dipole separation ( = in our case)
The grey line refers to the depth at which we measure the E-field corresponding the maximum of the cascade shower.
*we have modeled the detectors at 20m and 100m.
Notes: !Put the phase factor!

## Slide 6: Reason for optimizing
When we steer a phased array in vacuum, we lose power output to side lobes1,2. So, steering the array directly at the surface may cause a weak signal at the surface.
In addition, Antarctica has a non uniform index of refraction which causes the electric field to bend3. We want to control this bending so the field doesn’t drop off along the surface.
So, we want to find the optimal depth and steering angle of the array that minimize these effects and get a large power output along as much of the surface as possible.
1
2
3

## Slide 7: Optimization metric
We want to maximize a weighted area of the region along the surface where the power output from the phased array is above some threshold.
To find the region where the power output is above a certain threshold, we use two methods
Absolute threshold
dBd threshold
  Compare the phased array to a dipole.
if,
if,
* We tested with different values for and

## Slide 8: Optimization metric
We will use four methods for the weights These are used because we want to weight the regions close to the surface detectors higher.
The different methods
  Actual Area: Ignore the detectors and just calculate the actual area of
  Punished Short: Punish the area elements further from the short-range detector
  Punished Long: Same for the long-range detector
  Averaged Punished: Punish the area elements further from both detectors

## Slide 9: Optimization
We will use heat maps to view the area calculated by each combination of depth and steering angle.
We will start be comparing the simulations using finite difference time domain software1 and with ParaProp2. ParaProp is much faster, though less accurate than FDTD to the actual results.
In these initial tests we just used the actual area method to find the areas. And used a course scan of parameters
1: We used Meep and the code for this is found in optimizerNAnpyMeep1.py and optimizerNAnpyMeep2.py
2: This code is found in ParaPropPhasedArrayOptimization.ipynb

## Slide 10: Verify ParaProp
We initially looked at a slice of the electric field taken at a range using both ParaProp and FDTD (Meep).

## Slide 11: Verify ParaProp
We then looked at heat maps using both solvers.
FDTD
  PProp
        FDTD
        DbD Db
Notes: The source profiles are different in paraProp leading to these differences.

## Slide 12: Verify ParaProp
I have highlighted the best designs i.e. the designs with the maximized area in yellow from both solver methods.
We found good matchup between the two solver methods and will therefore use ParaProp throughout the rest of the optimization.
Notes: The source profiles are different in paraProp leading to these differences.

## Slide 13: Optimization results overview
I ran optimizations using all area methods and a more detailed set of parameters
  Depths [0m:20m by 1m] and angles [10:40 by 1]
Since there is no theoretical value for the threshold cutoff value, we tried multiple values.
We looked at the heat maps generated from each run. We got 4 maps for a given threshold.
Here’s how I analyzed the results
  I only looked at threshold values higher than a critically low value . is the lowest possible value that gives a single best design that gives the maximum area.
  I took the mode of all the designs from the different area methods from these thresholds.
  I then took the mode of the designs each area method converged at its critical threshold.
Notes: The source profiles are different in paraProp leading to these differences.

## Slide 14: Optimization results overview
I found that the optimal parameters were
This is mode of all the designs from all area and thresholds methods.
This is also the value all the “abs” threshold area methods converge on at the critical thresholds .
The “dBd” threshold area methods don’t all converge on this design at the critical threshold . But during the course of the project, we had felt that “dBd” was not as useful or accurate as “abs”. So, we excluded it from further use.
Depth: 6m Angle: 27
Notes: The source profiles are different in paraProp leading to these differences.

## Slide 15: Optimization results analysis
To see the convergence, I’ll show GIFs of the heat maps for each area method at different thresholds.
Also, I converted each best area configuration from a given threshold and area method to a numerical code and plotted them against the thresholds.
_ __
Depth Angle
→
→
6 27

## Slide 16: Heat Maps (Actual Area)

## Slide 17: Code vs. Threshold (Actual Area)
Chart: Actual Area
| 60 | 62 | 64 | 65 | 66 | 67 | 68
Field2 | 17 | 427 | 729 | 930 | 930 | 729 | 627
This shows the convergence of the design code at the critical threshold ()

## Slide 18: Best E Fields
930
017
627

## Slide 19: Heat Maps (Averaged Punished Area)

## Slide 20: Code vs. Threshold (Averaged Punished Area)
This shows the convergence of the design code at the critical threshold ()
Chart: Averaged Punished Area
| 60 | 62 | 64 | 65 | 66 | 67 | 68
Field2 | 17 | 18 | 1434 | 1132 | 930 | 831 | 627

## Slide 21: Best E Fields
1434
017
627

## Slide 22: Heat Maps (Punished @ 20m Area)

## Slide 23: Code vs. Threshold (Punished @ 20m Area)
This shows the convergence of the design code at the critical threshold ()
Chart: Punished at 20m
| 60 | 62 | 64 | 65 | 66 | 67 | 68
Field2 | 17 | 18 | 426 | 527 | 628 | 729 | 627

## Slide 24: Best E Fields
729
017
627

## Slide 25: Heat Maps (Punished @ 100m Area)

## Slide 26: Code vs. Threshold (Punished @ 100m Area)
This shows the convergence of the design code at the critical threshold ()
Chart: Punished at 100m
| 60 | 62 | 64 | 65 | 66 | 67 | 68
Field2 | 17 | 1434 | 1434 | 1131 | 930 | 831 | 627

## Slide 27: Best E Fields
1434
017
627

## Slide 28: Next Steps
Using an exponential function for the dipole depths of the form,
seems to suppress side lobes and concentrate
more power towards the surface.
  refers to the th antenna in the array
  is the dipoles wavelength
  is the depth of the top antenna which would
  still be optimized
  is a new optimized parameter.

## Slide 29: Conclusion and Next Steps (cont.)
Using an exponential function for the dipole phases of the form,
seems to concentrate the two beams power
  refers to the th antenna in the array
  is a new optimized parameter
Adding the detectors into the simulation
and simultaneously optimizing them and
the phased array could improve the
overall design.